The goals of this lab were to become familiar with communicating with instruments using Python, and to calibrate and use a thermistor to make measurements of temperature. To accomplish the first goal, we used a digital multimeter (DMM) to measure resistance, current, and voltage on a simple two resistor circuit, drawn below:

After having obtained the resistance of and voltage across both resistors, and the total current of the circuit, we used Ohm’s law to calculate the theoretical values for each corresponding measured value, and found that the values the DMM measured were within an acceptable range of the theoretical values (see tables A through D in Appendix A).

A thermistor is a type of thermometer that measures temperature based on its resistivity. By putting the thermistor in thermal contact with another substance and letting the thermistor’s temperature come to the temperature of the object we want to measure, we calculate that temperature if we know the resistance of the thermistor at that time. This equation is called the Steinhart-Hart equation:

where a, b, and c are unique to a given thermistor. In order to find a, b, and c, we had to make measurements of the temperatures of cold, room temperature, and boiling water and the resistance of the thermistor at those temperatures (See Table E in Appendix A), which gave us a system of 3 equations with 3 unknowns. We solved this system of equations using Python, yielding:

Once we had our equation calibrated, we used it to solve the following scenario:

Someday your boss may send you to fetch a piping hot coffee with just the right amount of half and half. But when should the cold half and half be added so the coffee is as hot as possible when the boss drinks it? At the café before walking back to the office? Or at the office after the walk back? Determine the answer experimentally.

To test this, we assumed that the boss liked their coffee with lots of cream, and that the walk back to the office was about 5 minutes in duration. We used cool and hot water as substitutes for cream and coffee. We measured the resistance of the thermistor in the cool water and the hot water at the beginning of each scenario, and then again at the end of the five minutes. For the case where the cool water is added to the hot water at the end of the five minutes, we found that the change in temperature for water added at the beginning of the five minute was -39.K and the temperature change for water added at the end of the five minutes was -43.7K, so it is better to add the creamer as soon as possible in order for the coffee to be as hot as possible at the end of the five minutes (see Appendix A, Table F).

Appendix A: Data and Error
We first measured the resistance for resistor 2 and then resistor 3 (there is no resistor 1, we just didn’t bother to change the 2 suffix on the first data file the first time we measured the resistance, so we called the other resistor 3).

Table A: Resistor 2 Resistance and Voltage
Resistor 2	1	2	3	4	5	Average
Resistance (Ohms)	1.05133817999999e+04	1.05133935999999e+04	1.05134102000000e+04	1.05135244000000e+04	1.05133690999999e+04	1.05134158199999e+04
Voltage (Volts)	3.10839549999999e+00	3.10838839999999e+00	3.10837340000000e+00	3.10840529999999e+00	3.10841669999999e+00	3.10839585999999e+00

Table B: Resistor 3 Resistance and Voltage
Resistor 3	1	2	3	4	5	Average
Resistance (Ohms)	9.10389708999999e+01	9.10372160999999e+01	9.10372694999999e+01	9.10383070999999e+01	9.10389861999999e+01	9.10381499599999e+01
Voltage (Volts)	2.71075999999999e-02	2.71080000000000e-02	2.71092999999999e-02	2.71096000000000e-02	2.71080999999999e-02	2.71085199999999e-02

Table C: Circuit Current and Battery voltage
	1	2	3	4	5	Average
Current (Amps)	2.95599999999999e-04	2.95599999999999e-04	2.95599999999999e-04	2.95599999999999e-04	2.95599999999999e-04	2.95599999999999e-04
Voltage (Volts)	3.13534870000000e+00	3.13536709999999e+00	3.13536329999999e+00	3.13529409999999e+00	3.13532089999999e+00	3.13533881999999e+00

Table D: Effective and Theoretical Values
	Effective	Theoretical	Percent error
Resistance	1.06044539699599E+04	1.06066942489851E+04	0.0211213689450347
Voltage (measured)	3.13533881999999E+00	3.13467659352014E+00	0.0211258310097785
Voltage (added)	3.13550437999999E+00	3.13467659352014E+00	0.0264073965895375
Current	2.95599999999999E-04	2.95662447956464E-04	0.0211213689341001

Table F: Thermistor Resistance at Different temperatures
	273.2K (cold water)	294.8K (room temp)	351.4K(hot water)
Resistance (Ohms)	3.300E+04	1.199E+04	1.923E+03

Table E: Resistances and temperatures of Hot and Cold water for coffee scenario
	Cool water (combine at t=0)	Hot water (combine at t=0)	Cool water (combine at t=5min)	Hot water (combine at t=5min)
Resistance (at t=0) (Ohms)	11600	1250	11600	1730
Temperature (at t=0) (K)	252.8761301	355.6157243	252.8761301	369.4092509
Resistance (at t=5min) (Ohms)	N/A	5730	N/A	3960
Temperature (at t=5min) (K)	N/A	316.3107333	N/A	325.7177938
Change in temperature (K)	N/A	-39.30499095	N/A	-43.69145713

It was not possible to measure the resistance at the immediate times listed (actual measurements took anywhere from 10s to a minute), but we were consistent with the time deviance for both scenarios.