The purpose of this lab was to investigate the photoelectric effect, and in the process make a measurement of the ratio of Plank’s constant (h) and the quantum of charge (e).

The photoelectric effect is a process by which electrons are emitted from a metals surface when the metal is hit by photons. The maximum kinetic energy of the emitted electrons (just after being emitted) is K= hc/λ -W, where W is the work function, λ is the wavelength of the photon, h is Planck’s constant and c is the speed of light. The value of W depends on the metal used. Our experimental setup consisted of a thin anode wire and a large area cathode all contained in an evacuated class envelope. When light hits the cathode, electrons are are emitted and collected by the anode and these electrons flow back to the cathode, which creates a measurable current. As electrons are emitted from the cathode and collected by the anode, the cathode and anode become, positively and negatively charged, respectively, which generates an electric field, and thus a voltage, between them. The initial kinetic energy of an electron that moves against an electric field from an initial voltage V1 to a final voltage V2 is e*(V2-V1), where e is the quantum of charge. By manipulating the voltage between the cathode and anode, we can find a stopping voltage, Vstop, where the electron has just enough energy to be collected by the anode. In this case the initial voltage is zero, and the final voltage is Vstop, so the initial kinetic energy of an emitted electron is e*Vstop. We can determine the stopping voltage by changing the applied voltage until the measured photocurrent goes to zero. Substituting e*Vstop for K, we get e*Vstop=hc/λ -W.

We obtain a h/e term by dividing both sides by e, yielding Vstop=(h/e)*(c/λ) -W/e. In this experiment, we shot lasers with wavelengths of 638nm, 532nm, and 446nm at a photocathode coated with Cs3Sb, which has a work function W=1.7eV, and found values for stopping voltages for each. Our data is complied in the following table.

Table A: Stopping voltages for different wavelengths of light
Stopping voltages	638nm	532nm	446nm
1	.69V	1.03V	1.52V
2	.68V	1.01V	1.62V
3	.64V	0.94V	1.57V

Using this data and the function Vstop=(h/e)*(c/λ) -W/e, we used python to find parameters for a function of the form F = a*x + b, where a = (h/e) one of our parameters, x=(c/λ) our independent variables, and b = -W/e another of our parameters. Our fitting coefficents were a = 4.4689208267884675e-15 +/- 5.32674118069505e-16, b = -1.465 +/- 0.306. The literature value of h/e is 4.1375e-15 J*s/C, and the calculated value of -W/e is 1.7 J/C. The literature values are within the range of variance of the fit values. A possible source of the variance within the fit values is the intensity of the blue light relative to the maximum stopping voltage, which could have given us a higher than expected value for the stopping voltage of blue light. Another possible source is inconsistency with the angle at which the different lasers were set up at to hit the cathode, which would cause the electrons emitted between different wavelengths of light to have different trajectories, which would effect what we get for a stopping voltage.