Introduction:
In this lab, we demonstrated that electrons diffract from a crystalline powder in the same manner as xrays, scattering strongly at certain angles. This lab had four goals:
1) Confirm the de Broglie wavelength-momentum relationship for electrons.
2) Show that graphite has a hexagonal structure.
3) Find the bond length a for carbon graphite
4) Compare your results (best value and uncertainty at the 2σ level) with a literature value.

Background;
The de Broglie hypothesis states that a quanton behaves like waves of wavelength λ=h/p, where h is Planck’s constant and p is the quanton’s relativistic momentum. In this experiment, a beam is formed from thermionically emitted electrons (of fundamental charge e = 1.602*10^-19 C) accelerated across large accelerating voltage (V) (but less that 5kV to keep the electrons from moving at any appreciable fraction of the speed of light, c), giving the electrons a kinetic energy K= e*V = p^2/2m[1], where m is the mass of an electron. Solving for p, we get p=√(e*V*2*m). Plugging this into our expression for the de Broglie wavelength, we get λ=h/√(e*V*2*m)=h*c/√(e*V*2*m*c^2), where m*c^2 = 5.11*10^5 eV, hc = 1240 eV*nm.
[1] This is an approximation for the kinetic energy for quantons whosse velocity v<<c

Bragg diffraction describes the process by which electrons scatter from a crystal, that is that they scatter weakly in all directions and strongly at angles that correspond to planes of atoms in phase, and these strongly scattered electrons constructively interfere. Much like the path length approximation we used to model double slit interference, Bragg’s law relates the wavelength of electrons scattered from a single crystal to the distance between atomic planes d and the scattering angle φ, by λ=2*d*sin(φ). In this case, we are shooting electrons not at a single crystal but at a crystal powder, giving us many small crystals in many different orientations. The Bragg condition from the set of all the planes which electrons are diffracted from leads to a diffracted beam that is conical, with half angle θ=2φ relative to the incident beam (see Figure A(a))
Figure A

As shown in Figure A(b), the diffracted electrons hit the a phosphor screen on the inner surface of a 41cm in circumference evacuated glass sphere, which allowed us to measure the angular diameter of the interference rings. Generally, diffracted waves have smaller deflection when their scattering surfaces are farther apart. Thus the two rings which we measured the angular diameter of correspond to the two largest spacings between planes of atoms in phase (see Figure B), with the inner ring corresponding to the largest spacing (d2) and the outer ring corresponding to the second largest spacing (d1). We hypothesized that the structure of the graphite power was hexagonal, leading to plane spacing values of d1=(a*√3)/2 and d2=3*a/2.
Figure B(hexagon plane)

Methods:
We measured 17 values for the angular diameters of each ring by varying the accelerating voltage between 2000 and 5000 volts. In order to avoid drift effects, we varied the values of the accelerating voltage up and down (see ). A magnet was attached to the base of the evacuated glass sphere near the electron gun to keep the incident beam properly centered on the phosphor screen.

Data analysis (from python):