The goal of this lab was to verify the spectral lines of hydrogen match the predictions of quantum mechanics and to determine the mass of the deuterium nucleus relative to the proton mass by measuring the wavelengths of the emission from a hydrogen-deuterium gaseous discharge tube.

Electrons in a hydrogen-like gas can be excited by running an electrical current though the gas. This causes the electrons to “jump” to a higher energy level (the actual change in the energy of the electron is an integer multiple of its ground state energy), and when the electron “drops” back down to a lower energy level, a photon with an energy corresponding to the change in energy is released. This energy corresponds to a wavelength, given by
 (RYDBERG FORMULA)
where RH is the Rydberg constant = 1.0973731568608*10^-2 nm^-, nf and ni are the final and initial energy levels, respectively.

In this experiment we found the Balmer series (n=2 transition energies) for Hydrogen and Deuterium. 1000VDC is run through a hydrogen-deuterium mixture in a sealed glass tube and direct the photons through a focusing lens into the aperture of a monochromator which feeds into a photomultiplier tube that sends current to an electrometer with which we communicate through Python. We did a survey scan at an aperture width of 15 micrometers to get a general idea of where the energy peaks would be (see figure 1a) and then optimzed the light instensity using our Python program. We then took precise, slow scans at an aperture width of 2 micrometers (See fig 1b-e), and our results are tabulated below
Table A: Raw Peaks of Hydrogen and Deuterium
Hydrogen Peak(nm)	Deuterium Peak(nm)
411.126	411.032
434.965	434.868
486.984	486.873
657.094	656.948

This experinent was not done a vacuum, so in order to check our data with the predictions of quantum mechanics, we multiplied them by the refrative index of air (1.0003):

Table B: Vacuum Corrected Peaks of Hydrogen and Deuterium
Hydrogen(nm)	Deuterium(nm)
411.242	411.148
435.087	434.990
487.120	487.009
657.276	657.129

We used python to fit our data against the energy level function. The value of our Rydberg constant was 0.010948 nm^-1 whereas the literature value was 0.010973731568508 nm^-1, giving us a percent error of +/- 0.2%. Ther error value is low enough that this error can be attributed to the precsision of the experiment.

Our second objective was to calculate the mass of the deuteron. We know from classical mechanics that the electron and nucleus must revolve around a common center of mass which is very close to the proton because mp>>me. To include the effect of the finite mass in the theory, the mass of the electron is replaced by the hydrgogen-atom system, defined by

We used Python to cacluclate the mass of the deuterium nucleus based on our data, and determined the value to be 1.71783amu with a percent error of 14.7% (standard deviation of +/-0.013622amu). Possible sources of error include the